## Slide 1: Balancing Performance With Building & Occupant Health
Peter Brown, Director Building Performance & Optimisation
CIBSE Measuring performance & facilities Management – session 2

## Slide 2: Savills BP&O
introduction
Building Performance & Optimisation
ENERGY CONSULTANCY
Air Conditioning Inspections (TM44)
Energy Audits
Heat Networks
Energy Performance Certificates (EPC+)
ESOS & SECR
Net Zero
GENERAL
Water Audits
Metering
Optimisation
BMS / BACS
SECR
NABERS

## Slide 3: Optimisation & Building Analytics
Process
Data collection
Familiarisation with BMS & Site
Locate historical data & download
Analysis
Create a model from aggregated BMS data
Interpretation
Prioritise measures
Discussions with facilities management
Outputs
Action list
Data model
Report
Obtain building energy data
Draft optimisation measures & assign actions
Analyse trends to identify improvement measures
Generate thermal model
Run scenario models to quantify impacts improvement measures

## Slide 4: Demand Based Ventilation
Data Analysis
Health & Wellbeing | Building Performance | Balance
Good internal air quality. | Over-ventilation with associated heating & cooling of incoming air. | Adapt Ventilation to VAV. £6,922 pa

## Slide 5: Ventilation
Data Analysis
Health & Wellbeing | Building Performance | Balance
Control of air quality. (Well Target 800ppm) | Overventilation, heating and cooling for make-up air. | Change AHU schedule & adjust PPM level £62,000 pa

## Slide 6: Ventilation
Data Analysis
Maximum Outdoor CO2 con. (ppm)
Current minimum supply fan speed 50%
Health & Wellbeing | Building Performance | Balance
Control of air quality. (Well Target 800ppm) | Overventilation, heating and cooling for make-up air. | Reduce AHU output, schedule & adjust PPM level £TBC

## Slide 7: Ventilation / Operating Hours
Data Analysis

## Slide 8: Building Over-Pressurisation
Data Analysis
Health & Wellbeing | Building Performance | Balance
Reducing draughts from infiltration. | Over pressurisation is 13%, missed opportunity to recover heat. | Re-pressure test and adjust ventilation rates. £711 pa

## Slide 9: Toilet Extract Ventilation
CASE Study
Health & Wellbeing | Building Performance | Balance
Control of air quality. | Overventilation, heating and cooling for make-up air. | PIR / occupancy control £22,200 pa

## Slide 10: Reception Heating
Data Analysis
Health & Wellbeing | Building Performance | Balance
Warm reception staff. | Heat wasted into upper atrium. | Stop draughts & lower htg setpoint. £5,738 pa

## Slide 11: Office Space Temperature Overheating
Data Analysis
Health & Wellbeing | Building Performance | Balance
Temperature control. | Wasted heat. | AHU setpoints, global resets £23,575

## Slide 12: FCU Control
Data Analysis
Health & Wellbeing | Building Performance | Balance
Temperature control. | Simultaneous heating & cooling. | Tenant engagement, AHU setpoint, global resets £29,750

## Slide 13: Mall Lighting & Dimming
Data Analysis
 | Mon-Fri |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Saturday |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Sunday |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Store opening times |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ODEON-Cinema |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
WC lights schedule |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cleaning Lighting |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cornice Lighting |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Mall Lighting |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Xmas Lighting |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 00:00 |  | 01:00 |  | 02:00 |  | 03:00 |  | 04:00 |  | 05:00 |  | 05:00 |  | 06:00 |  | 07:00 |  | 08:00 |  | 09:00 |  | 10:00 |  | 11:00 |  | 12:00 |  | 13:00 |  | 14:00 |  | 15:00 |  | 16:00 |  | 17:00 |  | 18:00 |  | 19:00 |  | 20:00 |  | 21:00 |  | 22:00 |  | 23:00 |  | 00:00 |  | 01:00 |  | 02:00 |  | 03:00 |  | 04:00 |  | 05:00 |  | 05:00 |  | 06:00 |  | 07:00 |  | 08:00 |  | 09:00 |  | 10:00 |  | 11:00 |  | 12:00 |  | 13:00 |  | 14:00 |  | 15:00 |  | 16:00 |  | 17:00 |  | 18:00 |  | 19:00 |  | 20:00 |  | 21:00 |  | 22:00 |  | 23:00 |  | 00:00 |  | 01:00 |  | 02:00 |  | 03:00 |  | 04:00 |  | 05:00 |  | 05:00 |  | 06:00 |  | 07:00 |  | 08:00 |  | 09:00 |  | 10:00 |  | 11:00 |  | 12:00 |  | 13:00 |  | 14:00 |  | 15:00 |  | 16:00 |  | 17:00 |  | 18:00 |  | 19:00 |  | 20:00 |  | 21:00 |  | 22:00 |  | 23:00 | 
Reduction in Lighting Output – dimming periods
Christmas Lights Off In Summer
Health & Wellbeing | Building Performance | Balance
Merchandising sales / bright & airy. | Wasted power during daylight hours. | Basic daylight dimming. £9,130

## Slide 14: Circadian Lighting
Data Analysis
Health & Wellbeing | Building Performance | Balance
Diurnal lighting output | Wasted power during daylight hours. | Energy saving = 10-30% Maintenance = 10-20% Productivity = 2-10%

## Slide 15: Optimisation Potential
Summary of Measures
Energy Savings: | 11%
Cost Savings: | £65.5k
CO2 Savings: | 72,000 kgCO2/yr

## Slide 16
Thanks
peter.brown@savills.com